## Slide 1: ILC 超伝導加速器技術 今後の開発にむけて（案）
山本 明・山口誠哉
（LC計画推進室・加速器研究施設）
2012-6-11

## Slide 2: アウトライン
超伝導加速空洞加速電界性能の進展
KEK-STF 超伝導加速器開発の進展
今後のさらなる開発推進にむけて

## Slide 3: Plan and Progress in SCRF/ATF
Year | 07 | 2008 |  | 2009 |  | 2010 |  | 2011 | 2012
Phase | TDP-1 |  |  |  |  |  | TDP-2 |  | 
Cavity Gradient in v. test to reach 35 MV/m |  Yield 50% |  |  |  |  |  |  Yield 90% |  | 
Cavity-string to reach 31.5 MV/m, with one-cryomodule |  | Global effort for string assembly and test (DESY, FNAL, INFN, KEK) |  |  |  |  |  |  | 
System Test with beam acceleration |  |  | FLASH (DESY) , NML (FNAL) STF2 / ATF (KEK) |  |  |  |  |  | 
Preparation for Industrialization |  |  |  |  | Production Technology R&D |  |  |  | 
Communication with industry: | 2011-2012: Mass production studies in contract |  |  |  |  |  |  |  | 
We are here

## Slide 4: Progress Integrated in Cavity Gradient Yield Updated, April., 24, 2012
Plot courtesy
Camille Ginsburg of FNAL
TDP-2 Goal
Being
saturated
35 MV/m usable

## Slide 5: Yearly Progress in Cavity Gradient Yield as of April 24, 2012
Yield ’10 ~ ’12:
~ 85% @ 25 MV/m
~ 80% @ 28 MV/m
~ 70% @ 35 MV/m
Yield in ’08 ~ ’09:
~ 70% @ 25 MV/m
~ 46% @ 35 MV/m

## Slide 6
Björn Wiik
vision
Under construction
Under construction
TDR by 2012
R&D needed
Continued progress in SRF gradient : breakthrough of 45 MV/m in 1-cell, ~60 MV/m record; 45 MV/m in 9-cell
GDE began in 2005: produce a design for ILC and coordinate worldwide R&D efforts
New SRF Test Facilities in operation: STF at KEK and NML at Fermilab
Upgrade of CEBAF to 12 GeV underway at Jefferson Lab (80 cavities)
FLASH operation and construction of European XFEL underway (640 cavities)
ITRP Recommendation
SCRF Cavity Gradient Progress
Courtesy: R. Geng

## Slide 7: 超伝導加速器システム・開発の進展 2009 ~
“9mA experiment”
achieved ~1800 bunches at 9mA in 09.2009
DE/ERMS ~0.5% (@ 0.8 GeV)
~0.1% within pulse
Full systems integration testing
FLASH (DESY)
NML (FNAL)
STF (KEK)
TDP focus
Under construction
Up to 6 cryomodules
Operation: end 2012
“Quantum Beam” experiment 2011
1 CM with beam 2013
7 CM → 1.2 GeV beam
photon user facility
(2 CM 2015)
(3 CM)

## Slide 8: S1-Global Assembly/Test with Global Effort
DESY, FNAL, Jan., 2010
INFN
and
FNAL
Feb.
2010
FNAL & INFN, July, 2010
DESY, May, 2010
March, 2010
June, 2010 ~
DESY, Sept. 2010

## Slide 9
MHI-09
MHI-07
MHI-06
MHI-05
AES004
ACC011
Z108
Z109
FNAL
DESY
KEK
S1-Global における空洞性能の経過
ave. Eacc,max
VT : 30 MV/m
1 cav : 27 MV/m
7 cav : 26 MV/m
D
C
D : Detune
C : Coupler
D
Performance reduction in two cavities and one coupler
Tuner mechanics trouble in two cavities

## Slide 10
Cavity : Capture Module(2 cavities）
+CM1(8 cavities）
+CM2(8 cavities）
Beam : 1ms, 9mA, 5Hz
RF-gun exit: 4.7MeV
Capture Module exit :21MeV,
CM1 exit：273MeV
CM2 exit：525MeV
RF-gun operation： 41.4MV/m (3.5MW input power）
Cavity operation : Capture Module : 15.2MV/m
CM1 : 31.5MV/m
CM2 : 31.5MV/m
STF Phase 2 accelerator
STF phase-2 accelerator is the beam test facility
which include electron gun and chain of ILC cryomodules.
The performance test of ILC cryomodule is a main target.
Full module or
half-modules ?

## Slide 11
STF-2 計画＠KEK
Capture Cryomodule
(two 9-cell cavities)
2012’, Feb. Cool-down
STF-2 #1 Cryomodule
(eight 9-cell cavities)
2014’, Jan. Cool-down

## Slide 12
KEK-STF
Quantum-Beam Accelerator
STF Quantum-Beam experiment
2012. Feb : cool-down started,
April : beam acceleration
High-flux X-ray by Inverse-Comton scattering
10mA electron beam （40MeV, １ｍｓ, ５Ｈｚ）
4-mirror laser resonator cavity
head-on collision with beam
Target: 1.3 x 1010 photons/sec 1%bandwidth
Capture cryomodule ( 2 SC cavities )
collision point
(Laser, electron beam)
photocathode RFgun
Beam acceleration (40 MV) and transport for 1 ms, successful !
April, 2012

## Slide 13
STF Plans
CY2011
CY2012
CY2013
CY2014
S1-Global cryomodule
STF phase-2
Phase2 Injector part
(Quantum-Beam experiment)
1st Cryomodule
Phase2 CM-2
or CM-1 cavity swap to new
phase2 injector
Phase2 ILC Cryomodule (CM-1)
CFF
construction and start-up
operation (2~4 cavities/year)
operation
operation
operation
1st cavity
2nd cavity, 3rd, 4th, ….
finish in Feb.
CY2015
CY2016
dis-assembly
sawp
cavities
Cryomodule test continuation
beam commissioning
Cryomodule commissioning
industrialization in operation
operation
sawp
cavities
operation
Presented by
H. Hayano

## Slide 14
STF-2 計画＠KEK
1. Capture Cryomodule (2)
2. Capture Cryomodule (2) + STF-2 #1 Cryomodule (8)
3-a. Capture Cryomodule (2) + STF-2 #1 Cryomodule (8)
+ STF-2 #2 Cryomodule (4) + #3 Cryomodule (4)
3-b. Capture Cryomodule (2) + STF-2 #2 Cryomodule (4) + #3 Cryomodule (4)
2 Cav.
2 Cav.
2 Cav.
2 Cav.
8 Cavities
8 Cavities
4 Cavities
4 Cavities
4 Cavities
4 Cavities
2012’, Feb. Cool-down
2014’, Jan. Cool-down
(2015’, Jan. Cool-down)
Under Discussion !!
(for Quantum-Beam Experiments)
(#1; for long cryomodule
performance)
(#2 ; for cost reduction)
(#3 ; for R & D)
Presented by
E. Kako

## Slide 15: STF2: Cavity Development Plan

## Slide 16
Compact ERL(cERL) project
 | Parameters
Beam energy | 35 - 200 MeV
Injection energy | 5 MeV
Average current | 10 - 100 mA
Acc. gradient (main linac) | 15 MV/m
Normalized emittance | 0.1 - 1 mm·mrad
Bunch length (rms) | 1 - 3 ps (usual) ~ 100 fs (with B.C.)
RF frequency | 1.3 GHz
Parameters of the Compact ERL
100 m
Demonstrate the technologies needed for future multi-GeV class ERL, and show its beam performances
ERL Development Building
KEK
35MeVで2013年にスタートその後、何らかの手段
でのエネルギー増強が望まれる。
K. Umemori

## Slide 17: cERL主加速部空洞への要求
ILCはパルス加速器、ERLはCW加速器。この違いのどれだけ対応できるかがポイント
空洞の加速勾配としては15～20MV/m(CW)を達成すること。
ビーム電流は10mAから始める可能性が高いが、近い将来に到達するであろう100mAの運転に対応すること。
15MV/mだと１台あたり約20W、４台だとすると約80Wの2Kでの熱負荷をハンドリングすること。
↓
空洞・周辺装置・クライオモジュール（＋冷凍機）が、Eacc=15MV/m, I=100mAのCW運転に対応したものであること。
K. Umemori

## Slide 18: STFからcERL 活用の可能性：まとめ
cERLへ流用する場合に問題となりそうなコンポーネント
  入力カップラー： Coupling, 冷却
  HOMカップラー： Heatingへの対策。HOM特性。
  クライオスタット： Heガスのハンドリング
検討が必要なコンポーネント
  空洞：（cutoff以上の周波数も含めたHOM特性評価）
（たぶん）問題無いであろうコンポーネント
  周波数チューナー
K. Umemori

## Slide 19: 今後の超伝導加速器 技術開発
STF
  超伝導加速空洞開発
    さらなる高電界の達成への努力：
    1-TeV アップグレードにおける電界目標：45 MV/m
  量子ビーム開発研究
    今年中に完了
  CM開発：CM1 からCM2 へ
    CM1: 2013に完成
  超伝導加速器技術開発の進展
    CM2 ~ : 4 連空洞、または8連空洞
    超伝導加速器としてのスタディー、ビーム利用
    cERLとの技術開発協力の可能性

## Slide 20: 開発協力の可能性
STF、cERL の協調開発
  STF: 超伝導加速空洞、CM の開発を牽引
  cERL：超伝導加速空洞・CMのビーム利用、検証
  1台の空洞開発を、2段階で活用
４連空洞CM開発
  開発設備投資の節約、現有設備の有効活用
  開発の素早いサイクル（地上組み立ての継続可）
  残る課題：実機長でのアラインメント等

## Slide 21: 課題
STF (パルス）>>> cERL(CW)
  中央部：共通化の可能性
  エンド：改造が必要
    高圧ガス設備の軽微な改造（エンド部のみ）の可能性
    梅森さんに、設計検討を依頼
    高圧ガス保安協会、茨城県との交渉、了解をえること
  時間スケール
    STF での開発：2012 ~ 2014
    cERL にむけた改造、CM組み立て、組み込み：~ 2015

## Slide 22: 超伝導加速空洞の開発進展、計画
2009 ~2012
  2台 (MHI) : 量子ビーム
  9台 (MHI)：STF, CM1
2012 ~
  4台 (MHI) ：CM2
2012 ~
  ~ 4台（入札：企業での製作）
    2 + 2 等の可能性：KEK-CFFを活用した製造の可能性含む
  ~ 2台（KEK-CFF：自作）

## Slide 23: 議 論
STF, cERL における超伝導加速空洞開発協力の可能性を探る
  1台の空洞を２回活かす努力
  転用可能な改造設計を探る
  人材、予算の有効活用効果の評価
外国製（FP7 High Gradient） Cavityの活用可能性
  高圧ガス設備としての認定が課題

## Slide 24: つづく
、、、

## Slide 25: 付記：高圧ガス保安協会への打診
高圧ガス製造設備としての空洞開発
  KEK自作空洞
  KEK 自作空洞のエンド部等の変更（改造）
  KEK 製造施設を活用した企業による製造
  外国製空洞の輸入／製造品の高圧ガス認定