# Description of the HPD test board for the VA-DAQ system

Version 1.0 - Bjorn Sundal - 22/5/00 – Last updated 22/5/00

Circuit ideas, system design and PCB layouts – Bjorn Sundal (BMS)

Schematics drawn by – Suleyman Azman (SAZ)

A total of N schematic sheets and M layout sheets are found in separate pdf-files.

Figure 1: Overview of component side of the 61 channel HPD readout board.

## Overview of the board

The board will be used to readout a 61channel proximity focused hybrid photodiode (HPD) by DEP. It has the DEP reference number PP0380.

The board is equipped with two pair of 32 channel VA/TA chips. The footprint fits the VA32C (or VA32C2) and TA32cg.

Only 61 of the available 64 VA/TA channels are connected. The channels not connected are the first one on the first VA/TA pair and the first and last channels on the second VA/TA pair.

The dimension of the board is 125mm by 95mm. The center of the 80 pin HPD connector (which will be plugged in on the backside of the card) is at the center of the 95mm edge but only 50mm from the edge. The 4 screw holes are 3mm size and are all centered 5mm in x and y from the corners.

The board can be interfaced towards a VA-DAQ readout system. It contains however the possibility of generating all analog biases on board such that a simplified readout system only providing power and digital control can be used.

The schematic and layout plots are found in separate pdf-files.

## Operation of the board

The connector J1 is a 50 pin ERNI connector that goes together with a 25mil flat cables, also used by the VA-DAQ system. Pin 1 is the lower left in figure 1, pin 2 is the upper left and up to pin 50, which is the upper right pin.

The pinout is as defined by the VA/TA standard connector for the VA-DAQ system. It is given in table 1 below.

| Pin | Signal |  | Pin | Signal |
| --- | --- | --- | --- | --- |
| 1 | Clkin |  | 2 | Regin |
| 3 | Regout |  | 4 | Teston |
| 5 | Shift_outb |  | 6 | n.c. |
| 7 | Ckb |  | 8 | Ck (dummy for c.m. reduction) |
| 9 | Shift_in (dummy for c.m. reduction) |  | 10 | Shift_in_b |
| 11 | Dresetb (dummy for c.m. reduction) |  | 12 | Dreset |
| 13 | Hold (dummy for c.m. reduction) |  | 14 | Holdb |
| 15 | DVDD |  | 16 | DGND |
| 17 | VDD |  | 18 | GND |
| 19 | DVSS |  | 20 | DGND |
| 21 | VSS |  | 22 | GND |
| 23 | VSS |  | 24 | GND |
| 25 | Outp |  | 26 | Outm |
| 27 | n.c. (To GND on VADAQ) |  | 28 | Ta |
| 29 | Tb |  | 30 | n.c. (To GND on VADAQ) |
| 31 | Cal |  | 32 | n.c. (To GND on VADAQ) |
| 33 | Refbi (Vref of on other VA/TA boards) |  | 34 | Vfp |
| 35 | Vfs |  | 36 | Ibuf |
| 37 | Sha_bias |  | 38 | Sbi (Pre_bias on other VA/TA boards) |
| 39 | Vfs_ta |  | 40 | Vrc_ta |
| 41 | Vthr |  | 42 | n.c. |
| 43 | n.c. |  | 44 | n.c. |
| 45 | n.c. |  | 46 | n.c. |
| 47 | n.c. |  | 48 | n.c. |
| 49 | Detector return |  | 50 | Detector bia |

Table 1: Pinout on the 50 pin ERNI connector for the HPD board.

## Mapping of VA/TA pin number and HPD pad number and pin number

The 61 pads of the HPD is shaped in an hexagonal structure as shown below in figure 2.

Figure 2:  HPD pad view from topside and the PCB footprint for the PG80 socket of the HPD.

Figure 2 also shows the footprint on a PCB for the HPD socket. If the HPD board is seen from the bottom side this is how it will look. Typically a PG80 socket (a 100mil pitch socket in 12 by 12 array where the inner 10 by 10 is unused) is mounted on the bottom side. This saves the HPD (which is expensive) from being permanently attached to the HPD readout board.

The 64 input channels of the two 32 channel  VA/TA chips are numbered 0 to 63 in the VADAQ software. The below table 2 lists the relationship between the HPD pad number the HPD socket pin number and the VA/TA channel number.

The remaining pins on the PG80 socket is used to provide the 60V (max) for the IN-side of the PIN diodes (pin K1, B2, C12 and L11) and to the guard ring of the diodes (M6 and A7), which is grounded close to the front-end chips. The remaining pins are not connected (M1, M2, L1, E2, B1, A1, A2, A11, A12, B12, M11, M12 and L12). As seen from the coordinates are these mostly the corner pins.

| Va/Ta ch# | HPD pad | HPD pin |  | Va/Ta ch# | HPD pad | HPD pin |  | HPD pad | Va/Ta ch# | HPD pin |  | HPD pad | Va/Ta ch# | HPD pin |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | None | None |  | 32 | None | None |  | None | 0 | None |  | 30 | 46 | F11 |
| 1 | 26 | H1 |  | 33 | 36 | E12 |  | None | 32 | None |  | 31 | 22 | H11 |
| 2 | 18 | J1 |  | 34 | 44 | D12 |  | None | 63 | None |  | 32 | 14 | G2 |
| 3 | 17 | K2 |  | 35 | 45 | C11 |  | 1 | 24 | M9 |  | 33 | 48 | F2 |
| 4 | 11 | L2 |  | 36 | 51 | B11 |  | 2 | 21 | M8 |  | 34 | 11 | G1 |
| 5 | 24 | J2 |  | 37 | 38 | D11 |  | 3 | 18 | M7 |  | 35 | 51 | F1 |
| 6 | 10 | L3 |  | 38 | 52 | B10 |  | 4 | 10 | M4 |  | 36 | 33 | E12 |
| 7 | 5 | M3 |  | 39 | 57 | A10 |  | 5 | 7 | M3 |  | 37 | 40 | E11 |
| 8 | 25 | H2 |  | 40 | 37 | E11 |  | 6 | 27 | M10 |  | 38 | 37 | D11 |
| 9 | 16 | L4 |  | 41 | 46 | B9 |  | 7 | 26 | L10 |  | 39 | 44 | B8 |
| 10 | 4 | M4 |  | 42 | 58 | A9 |  | 8 | 20 | L8 |  | 40 | 49 | B6 |
| 11 | 34 | G1 |  | 43 | 28 | F12 |  | 9 | 13 | M5 |  | 41 | 57 | D2 |
| 12 | 23 | L5 |  | 44 | 39 | B8 |  | 10 | 6 | L3 |  | 42 | 62 | D1 |
| 13 | 9 | M5 |  | 45 | 53 | A8 |  | 11 | 4 | L2 |  | 43 | 54 | E1 |
| 14 | 32 | G2 |  | 46 | 30 | F11 |  | 12 | 29 | K12 |  | 44 | 34 | D12 |
| 15 | 15 | L6 |  | 47 | 47 | B7 |  | 13 | 28 | K11 |  | 45 | 35 | C11 |
| 16 | 29 | G11 |  | 48 | 33 | F2 |  | 14 | 23 | L9 |  | 46 | 41 | B9 |
| 17 | 22 | L7 |  | 49 | 40 | B6 |  | 15 | 15 | L6 |  | 47 | 47 | B7 |
| 18 | 3 | M7 |  | 50 | 59 | A6 |  | 16 | 9 | L4 |  | 48 | 55 | B4 |
| 19 | 27 | G12 |  | 51 | 35 | F1 |  | 17 | 3 | K2 |  | 49 | 60 | C2 |
| 20 | 8 | L8 |  | 52 | 54 | B5 |  | 18 | 2 | J1 |  | 50 | 61¦ | C1 |
| 21 | 2 | M8 |  | 53 | 60 | A5 |  | 19 | 31 | H12 |  | 51 | 36 | B11 |
| 22 | 31 | H11 |  | 54 | 43 | E1 |  | 20 | 30 | J12 |  | 52 | 38 | B10 |
| 23 | 14 | L9 |  | 55 | 48 | B4 |  | 21 | 25 | J11 |  | 53 | 45 | A8 |
| 24 | 1 | M9 |  | 56 | 61 | A4 |  | 22 | 17 | L7 |  | 54 | 52 | B5 |
| 25 | 21 | J11 |  | 57 | 41 | D2 |  | 23 | 12 | L5 |  | 55 | 58 | B3 |
| 26 | 7 | L10 |  | 58 | 55 | B3 |  | 24 | 5 | J2 |  | 56 | 59 | A3 |
| 27 | 6 | M10 |  | 59 | 56 | A3 |  | 25 | 8 | H2 |  | 57 | 39 | A10 |
| 28 | 13 | K11 |  | 60 | 49 | C2 |  | 26 | 1 | H1 |  | 58 | 42 | A9 |
| 29 | 12 | K12 |  | 61¦ | 50 | C1 |  | 27 | 19 | G12 |  | 59 | 50 | A6 |
| 30 | 20 | J12 |  | 62 | 42 | D1 |  | 28 | 43 | F12 |  | 60 | 53 | A5 |
| 31 | 19 | H12 |  | 63 | None | None |  | 29 | 16 | G11 |  | 61 | 56 | A4 |

Table 2: Mapping between VA/TA channel number and HPD pad number (left half of table) and opposite mapping (right half of table).

## Component list for the VATAHPD board ver1.0

| Part | Value | IDE part | Description |
| --- | --- | --- | --- |
| Capacitors |
| C1, C2-C4 | 6u8_EIA6032 100n_SMD0603 | 492 480 | EIA6032 tantal capacitor. 0603 ceramic X7R capacitor. Decoupling of AVDD. |
| C5, C6-C8 | 6u8_EIA6032 100n_SMD0603 | 492 480 | EIA6032 tantal capacitor. 0603 ceramic X7R capacitor. Decoupling of AVSS. |
| C9, C10-C12 | 6u8_EIA6032 100n_SMD0603 | 492 480 | EIA6032 tantal capacitor. 0603 ceramic X7R capacitor. Decoupling of DVDD. |
| C13, C14-C16 | 6u8_EIA6032 100n_SMD0603 | 492 480 | EIA6032 tantal capacitor. 0603 ceramic X7R capacitor. Decoupling of DVSS. |
| CA1, CB1 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Gbi for TA pair A and B. |
| CA2, CB2 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Pre_bias for VA pair A and B. |
| CA3, CB3 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Otabi for VA pair A and B. |
| CA4, CB4 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Taobi for TA pair A and B. |
| CC1, CC2 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Vfsta for TA pair A and B. |
| CC3, CC4 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Vfs for VA pair A and B. |
| CC5 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. DO NOT MOUNT. Decoupling of ibuf for VA pair A and B. |
| CC6, CC7 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Refbi for TA pair A and B. |
| CC8, CC9 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Vfp for VA pair A and B. |
| CC10, CC11 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Sbi for TA pair A and B. |
| CC12, CC13 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Sha_bi for VA pair A and B. |
| CC14, CC15 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Vthr for TA pair A and B. |
| CC16, CC17 | 100n_SMD0603 | 480 | 0603 ceramic capacitor. Decoupling of Vrc for TA pair A and B. |
| CD1-CD4 | 220n_SMD1206 | 306 | Ceramic 1206 rated 100V. For PIN diode 60V decoupling. |
| CT1-CT2 | 1p80_SMD0603 | 775 | Ceramic 0603. For injection of test pulses. |
| Resistors |
| RA1, RB1 | 8k20_SMD0603 | 780 | 0603 resistor. Gbi for TA pair A and B. –330mV/203uA (default 200uA) |
| RA2, RB2 | 3k90_SMD0603 | 779 | 0603 resistor. Pre_bias for VA pair A and B. –240mV/575uA. (default 500uA) |
| RA3, RB3 | 33k0_SMD0603 | 784 | 0603 resistor. Otabi for VA pair A and B. –860mV/87uA. (default 40uA) |
| RA4, RB4 | 33k_SMD0603 | 784 | 0603 resistor. Taobi for TA pair A and B. -745mV/83uA. (default 90uA) |
| RC1, RC2 | 20k0_SMD0603 10k0_SMD0603 | 649 648 | 0603 resistor. Divider to generate Vfsta. 667mV/67uA. DO NOT MOUNT. |
| RC3, RC4 | 20k0_SMD0603 10k0_SMD0603 | 649 648 | 0603 resistor. Divider to generate Vfs. 667mV/67uA. DO NOT MOUNT. |
| RC5 | 15k0_SMD0603 | 700 | 0603 resistor. Ibuf for both VAs. -250mV/150uA. (default 140uA). DO NOT MOUNT. |
| RC6 | 22k0_SMD0603 | 783 | 0603 resistor. Refbi for TA pair A and B. DO NOT MOUNT. 50uA. (default 40-50uA/2chips) |
| RC7, RC8 | 4k70_SMD0603 20k0_SMD0603 | 570 649 | 0603 resistor. Divider to generate Vfp. -380mV/81uA. DO NOT MOUNT. |
| RC9 | 10k0_SMD0603 | 781 | 0603 resistor. Sbi for TA pair A and B. DO NOT MOUNT. 240uA. (default 240uA/2chips) |
| RC10 | 56k0_SMD0630 | 785 | 0603 resistor. Sha_bi for VA pair A and B. DO NOT MOUNT. 44uA. (default 44uA/2 chips) |
| RC11, RC12 | SMD0603 SMD0603 | - - | 0603 resistor. Can be used to select a fixed threshold. RC11 to AVDD and RC12 to AVSS. DO NOT MOUNT. |
| RC13, RC14 | 1k20_SMD0603 6k80_SMD0603 | 778 647 | 0603 resistor. Vrc for TA pair A and B. 1400mV/500uA. (nominal 1400mV) |
| RT1 | 51R0_SMD0603 | 776 | 0603 resistor. Terminating calibration pulse. |
| RT2 RT3 RT4 | 120R_SMD0603 | 777 | 0603 resistor. Terminating ck/ckb, hold/holdb and shiftin/shitinb, respectively |
| RP1 RP2 | SMD0603 | - - | 0603 resistor. Pull resistors to DVDD fro Ta/Tb in case differential will be used. DO NOT MOUNT. |
| RD1 | 0R00_SMD0603 | 708 | Connect if detector bias (60V) comes from VA-DAQ. DO NOT MOUNT. |
| RD2 | 0R00_SMD0603 | 708 | Connect if detector return (ref) to VA_DAQ. DO NOT MOUNT. |
| RD3 | 0R00_SMD0603 | 708 | Connects PIN diode guard to AGND. |
| RD4 | 0R00_SMD0603 | 708 | Connects shield of the dual LEMO J2 for the HV to AGND. DO NOT CONNECT. (Default is to solder wires to a LEMO mounted in the AL box). |
| RZ0 | 0R00_SMD0603 | 708 | Connects VADAQ bias0 to the board Vfsta. |
| RZ1 | 0R00_SMD0603 | 708 | Connects VADAQ bias1 to the board Vfs. |
| RZ2 | 0R00_SMD0603 | 708 | Connects VADAQ bias2 to the board Ibuf. |
| RZ3 | 0R00_SMD0603 | 708 | Connects VADAQ bias3 to the board Refbi. |
| RZ4 | 0R00_SMD0603 | 708 | Connects VADAQ bias4 to the board Vfp. |
| RZ5 | 0R00_SMD0603 | 708 | Connects VADAQ bias5 to the board Sbi. |
| RZ6 | 0R00_SMD0603 | 708 | Connects VADAQ bias6 to the board Sha_bi. |
| RZ7 | 0R00_SMD0603 | 708 | Connects VADAQ bias7 threshold network to the board Vthr. |
| RZ8 | 0R00_SMD0603 | 708 | Connects VADAQ adapter board Vrc bias to the board Vrc. DO NOT MOUNT (use internal board bias). |
| Pin rows, connectors and sockets |
| D1 | PG80 | ? | PG80 socket for HPD. MOUNT ON BACKSIDE. |
| J1 | ERNI50SS | ? | 50 pin ERNI, standing, straight for SMD. |
| J2 | LEMO2 | ? | 2 pole LEMO for PCB mount. DO NOT MOUNT. |
| Active components |
| U1,U2 | VA32c/TA32cg | ?VA ?TA | Mount a VA32c and a TA32cg. A VA32c2 chip can be bonded, but the current compensation circuitry must be strapped. |

The board is marked with DEVICE number 1035 and the name ‘VATAHPD’ Ver 1.0.

The bond diagram is found below.

Figure 3: Bond diagram for the VATAHPD board.

## Test results with the HPD board ver1.0

The below tests are performed with the board with serial 1035-1-1.

| Bias | Group A | Group B | Nominal |
| --- | --- | --- | --- |
| TA feedback resistance. - Vfsta, bias 0. |  |  | 700mV |
| VA feedback resistance of shaper. - Vfs, bias 1. |  |  | 700mV |
| VA output buffer gain. - Ibuf, bias 2. |  |  | 140uA |
| Step size of calibration DAC. - Refbi, bias 3. |  |  | 20-25uA/chip |
| Feedback resistance of preamp. - Vfp, bias 4. |  |  |  |
| Gain current in discriminator. - Sbi, bias 5. |  |  | 120uA/chip |
| VA shaper bias. - Shab, bias 6. |  |  | 22uA/chip |
| Trigger width bias. - Twb. Connected to AGND close to the TA. | 0 mV | 0 mV | 10uA |
| High pass filter for TA. - Vrc, generated on the board. Resistor divider between AVDD/AVSS. |  |  | 1400mV |
| Gain stage bias. - Gbi, internal in each group. |  |  | 200uA/chip |
| VA preamp bias. - Preb, internal in each group. |  |  | 500uA/chip |
| VA differential receivers. - Otabi, internal in each group. |  |  | 40uA/chip |
| TA discriminator bias. - Taobi, internal in each group |  |  | 90uA/chip |