## Slide 1: FPCCD Vertex Detector for ILC
Yasuhiro Sugimoto
KEK
@TILC08
Concept of FPCCD VTX
FPCCD prototype
VTX inner radius

## Slide 2: Basic concept
Pair background at small R
  ~5000 hits/cm2/train with B=3T and R=20mm
  Pixel occupancy ~10% for 25m pixel (several pixels are fired for one track hit)
  In order to keep the occupancy small (<1%),
    read out 20 times per train (1ms), or
    20 times finer pixel
  is necessary
 Fine Pixel CCD (FPCCD)

## Slide 3: Advantages of FPCCD VTX
Completely free from beam-induced RF noise (EMI)
Excellent spatial resolution of x~1.4m even with digital readout
Excellent two-track separation capability because of fine pixels and fully depleted epitaxial layer
Capability of low-energy pair-background rejection by making use of hit-cluster shape
Simple structure which enables large wafer size with high yield rate
No heat source in the image area
No need for very high readout speed

## Slide 4: Schematic design
Sensor and ASIC
  ~5m square pixel
  Multi-port readout to reduce readout time (<200ms) with moderate readout speed (~10Mpixels/s)
  Small number of V-shift and large number of H-shift to reduce effect of radiation damage (CTI)
  15 – 20 m thick fully depleted epitaxial layer

## Slide 5: R&D for FPCCD sensor
Challenges of FPCCD
  Small pixel size ~5 m
  Readout speed > 10 MHz
  Noise < 50 electrons (preferably <30 electrons)
  Power consumption < 10 mW/ch
  Horizontal register (same size as pixel) in the image area
  Wafer thickness ~50 m
  Multi-channel low power readout ASIC  Takubo’s talk
Prototype sensor in FY2007
  Tackle issues 2, 3, 4, and 5

## Slide 6: Prototype of FPCCD
12m pixel size
512x512 pixels
6.1x6.1 mm2 image area
4ch /chip
128(V)x512(H) pixels for each channel
Several different designs of output amp
Chips have been made and are being tested by HPK
To be delivered in few weeks
8.2 mm
7.5 mm

## Slide 7: Types of Prototype
Output amp: type A – H
Process / Device type
  Wafer: epitaxial layer 24 / 15 m
  Gate SiO2 for output Tr: standard (all) / thin (CP204, 205)
  Device type: package / bare chip

## Slide 8: Packaged and bare chip

## Slide 9: Output amp
Type D
Others
Type | M1 | M2 | M3
A | M1-Type1 | M2-Type1 | M3-Type1
B |  |  | M3-Type2
C |  |  | M3-Type3
E |  | M2-Type2 | M3-Type2
F |  |  | M3-Type3
G |  |  | M3-Type4
Ｈ |  | M2-Type1 | M3-Type4
Remark |  | Type1 > Type2 at drain current | Type1 > Type2 > Type3 > Type4 at drain current

## Slide 10: Characteristics of Prototype
Preliminary results given by HPK
Device type | Package |  | Bare chip | 
Epi thickness (m) | 15 | 24 | 15 | 24
V-register gate capacitance (pF) | 1600 | 550 | 1600 | 550
H-register gate capacitance (pF) | 40 | 40 | 40 | 40
Output source capacitance (pF) | <4 | <4 | <2 | <2
Amp type |  | A | B | C | E | F | G
Output gain (V/e) | Epi:15 m | 5.4 | 5.3 | 5.2 | 6.9 | 6.2 | 5.6
 | Epi:24 m | 5.8 | 5.3 | 5.0 | 6.6 | 5.9 | 5.4
Id (mA) | Epi:15 m | 1.57 | 1.55 | 1.50 | 1.28 | 1.22 | 1.14
 | Epi:24 m | 1.48 | 1.44 | 1.38 | 1.15 | 1.09 | 0.99
VOD=10V, RL=10k, 10MHz, RT

## Slide 11: Study on inner radius
Design criteria
  Reasonable clearance between pair-background core and beam pipe, and between beam pipe and ladder
B (T) | ECM (GeV) | Option | R0(mm) | R1(mm)
3 | 500 | Nominal | 13 | 17.5
3 | 500 | Low P | 17 | 22
Simulation by CAIN
B=3 T
Strong dependence on machine parameters
G1=2mm, G2=4mm, L1=5mm, L2=20mm
B (T) | R0(mm) | R1(mm)
3 | 13 | 17.5
3.5 | 12 | 16
4 | 11.5 | 15
(500GeV Nominal)

## Slide 12: Summary and outlook
The first prototype FPCCDs have been made by HPK and will be delivered soon
  Pixel size: 12m
  H-register same size as pixels in image area
  4ch/chip
  Several types of output circuit
  Two different epitaxial layer thickness (15 / 24 m)
  Two different gate oxide thickness for output transistors
Detailed study on the prototype FPCCDs will be done in FY2008
Radius of innermost layer Rin of VTX was studied for 3, 3.5, and 4T magnetic field, and Rin=17.5, 16, and 15 mm are proposed, respectively

## Slide 13: Backup slide

## Slide 14: Collaboration
KEK
  A. Miyamoto, K. Nakayoshi, Y. Sugimoto
JAXA/ISAS
  H. Ikeda
Tohoku University
  T. Nagamine, Y. Takubo, H. Yamamoto
Tohoku Gakuin University
  K. Abe

## Slide 15: FPCCD VTX
Vertex detector
  Two CCD layers make a ladder in order to make mini-vector of tracks and reject pair-background tracks
  3 ladders make the vertex detector
  Operation at ~-50 degrees
  Ladders are confined in a cryostat
  Angular coverage:
    |cos|<0.95 with inner 4 layers
    |cos|<0.9 with all 6 layers