## Slide 1: A new idea of the vertex detector for ILC
Y. Sugimoto
Nov.10. 2004

## Slide 2: Boundary Condition at ILC
Beam Structure
  337 ns between BXs
    Preferable for SIT, TPC, CAL in terms of bunch ID
  2820 BX/train (~x15 of GLC)
  5 trains/s (~1/30 of GLC)
  Lum/train: ~x40 of GLC
Pair Background
  TESLA Study (B=4T,R=15mm):
  ~3.5 hits/BX/cm2=100 hits/train/mm2
  Large Detector Study (B=3T,R=20mm):
  ~1.5 hits/BX/cm2=40 hits/train/mm2
Pixel Occupancy of the 1st layer of Vertex Detector
  Pixel size:25m  ~25% (TESLA)/ ~10% (LD) for 1 train (~4 pixels hit by a track hit)

## Slide 3: How to reduce pixel occupancy?
Read out >20 times per train
  Column parallel readout
    CPCCD (LCFI group)
    MAPS (Strasburg group)
    >50 MHz readout speed
    Possible RF pick-up problem
  Analog registers on pixel (Readout between trains)
    FAPS (RAL group): CMOS pixel with registers
    ISIS (LCFI group): Small CCD registers on pixel
    Complicated design  Mosaic of small segments
    Possible RF pick-up problem for FAPS
Use >20 times finer pixels  A new idea: Fine Pixel CCD

## Slide 4: Deign concept of FPCCD
Pixel size: 5m square
Accumulate 2820 BX and readout between trains
Fully depleted to suppress diffusion and reduce hit pixels
Pixel Occupancy < 0.5% at R=20mm and B=3T  Acceptable
Multi-port readout to reduce readout time and increase radiation immunity
Operation at low temperature (< -70 C) to suppress dark current accumulated in readout cycle time of 200ms

## Slide 5: Challenges of FPCCD
Pixel size
Tracking efficiency
Thin wafer
Lorentz angle
Readout electronics
Radiation hardness

## Slide 6: Challenges of FPCCD
Pixel size
  Our target (5m) is not extraordinary
  3m pixel CCDs are used for mobile phones
  2.2m pixel CCDs will be available soon for the digital camera application
  Although requirement for the performance is different from each other, 5m pixel size seems quite feasible
  Problem is “who WILL make it ?”

## Slide 7: Challenges of FPCCD
Tracking efficiency
  Pixel occupancy ~0.5%, but hit density is ~40/mm2
  Large number of background hits may cause tracking inefficiency: mis-identification of signal hit with background hit
 : Background hit density
0 : Multiple scattering angle
For a normal incident track;
Angular and momentum dependence;

## Slide 8: Challenges of FPCCD
Tracking efficiency
cos
pmis
d=10mm, =40/mm2
d=2mm, =40/mm2
d=10mm, =2/mm2
Mis-identification Probability (p=1 GeV/c,tSi=50m)

## Slide 9: Challenges of FPCCD
Tracking efficiency: Background rejection
  Background particles have much lower pt than signal tracks
  We can expect background rejection by hit cluster shape
  FPCCD has tracking capability with only one layer!

## Slide 10: Challenges of FPCCD
Thin wafer
  For low momentum particles, thin CCD wafer (<50 m) is crucial to get
    better impact parameter resolution
    better tracking efficiency
  Several ideas;
    Partially thinned wafer
    Stretched thin wafer
    Thin wafers on both sides of rigid foam
Partially thinned wafer

## Slide 11: Challenges of FPCCD
Lorentz angle
  Signal charge in fully depleted CCDs put in a B field moves with finite angle (Lorentz angle) with respect to E-field
  Signal charge could spread over several pixels due to this Lorentz angle
  If the Lorentz angle is small, it can be cancelled out by putting CCD wafers with a tilt angle same sa the Lorents angle

## Slide 12: Challenges of FPCCD
Readout electronics
  Small pixel  Small signal for inclined tracks (as small as ~500 electrons)
    Very low noise readout circuit is necessary
    Electron Multiplying CCD is an interesting option
  Multi-port readout  Multi channel readout ASIC
    Readout pitch: less than 1mm
    Variable gain amp, CDS, and 5 – 8 bit ADC for each channel (to keep dynamic range)
    Data compaction circuit

## Slide 13: Challenges of FPCCD
Radiation hardness
  Increase of dark current by radiation damage
    Room temperature operation of CCDs seems possible at GLC (6.7ms readout cycle time), but not practical at ILC (200ms readout cycle time) because of too much dark current accumulation
  Charge transfer inefficiency (CTI)
    Low temperature operation (~-80 C) is favorable from the viewpoint of CTI caused by radiation damage
    FPCCD has small charge transfer channel  Less CTI
    Radiation immunity of FPCCD for the use as a vertex detector at ILC has to be demonstrated

## Slide 14: Possible design of FPCCD vertex detector
Two layers make a doublet to pick up signal hits out of background hits
Pixel disks may be necessary in the small angle region (cos>0.9)
The whole detector is confined in a cryostat and cooled by nitrogen vapor

## Slide 15: Summary
We propose a totally unique (or ridiculous?) concept of a vertex detector for Cold Machine
  Fully depleted CCD with 5m-square fine pixel size
  Accumulate 2820 BX and readout between trains
  Two layers make a doublet (super layer) to pick up signal hits out of background hits
Expected performance;
  Pixel occupancy ~0.5%
  Wrong tracking probability less than 1% in cos < 0.9
Things to do;
  Tracking simulation
  Measurement of Lorentz angle (using large pixel F.D. CCD)
  etc.

## Slide 16: Proposed Options in EU
CMOS
  MAPS (Strasburg group)
    Readout 20 times/train
    Column parallel readout
    High speed readout
    RF pickup (?)
  FAPS (RAL group)
    8 registers/pixel achieved
    RF pickup during transfer from pixel to register (?)
    If >20 registers, it can be read out between trains

## Slide 17: Proposed Options (Cont.)
CCD (RAL and UK group)
  Column Parallel CCD
    Readout 20 times/train
    High Speed (>50MHz)
    RF Pickup (?)
  In-situ Storage Image Sensor (ISIS)
    Readout between trains
    Complicated design
    Cross-talk
Other options: DEPFET, SOI, etc.
All options assume the readout of 20 frames/train