## Slide 1: Beam background study for GLC
Tsukasa Aso, Toyama College of Maritime Technology
and GLC Vertex Group
H.Aihara, K.Tanabe, Tokyo Univ.
and BDS Group
Based on the studies at GLC Vertex Group
includes contribution from BDS Group
Notes: I talk about “Beam background study for GLC”.
First of all, I should mention that my talk based on the studies at GLC vertex group,
so that the background in this talk means a background for the vertex detector.

## Slide 2: Contents
Beam-Beam background for VTX
  Results from VTX Group
Upstream background
  Results from BDS Group
Summary
Notes: Contents of my talk is like this.

## Slide 3: Beam-Beam Background
Incoherent e+e- pair production
  Studied with CAIN MC generator
    Processes included in CAIN, Beam-Beam interaction
      Breit-Wheeler (gamma + gamma -> e- + e+)
      Beth-Heitler (gamma + e+- -> e+- + e- +e+)
      Landau-Lifshitz (e + e -> e + e + e- + e+ )
      Bremsstrahlung (e + e -> e + e + gamma)
Background situation depends on
    Beam parameters
    IP region design
    Detector magnetic field
We estimated the hit density on the VTX detector for some of the settings.
Notes: We studied the influence of incoherent e+e- pair production using CAIN MC generator.
The CAIN MC generator includes these processes, and predict final angular distributions
by computing electric field of the beam.
Final state momentum will change according to the beam parameters.
And, also the background situation will change depending on the interaction region designs and detector magnetic field.
So, we estimated the hit density on the VTX detector for some of settings.

## Slide 4: Property of Beam-Beam Interaction
TRC500 Beam parameter [Technical Review Committee]
  Beam Energy 250GeV
  Repetition rate 150 Hz
  Bunch population 0.75x1010
  Normalized emittance 360/4 (10-8rad m)
  Beam size at IP 243nm/3nm/110um
Crab crossing
  0mrad/7mrad/20mrad
    Current interest of crossing angle is a larger crossing angle, because of the design of final focus systems as well as beam dump systems
Head-on
Incoherent e+e- pair
Right going electron beam
produces spread-out positrons, since the same sign charge as the incoming positron beam.
Positrons
Electrons
~500mrad
~100mrad
z
x
Electron beam
Positron beam
electron
positron
Beam profile at IP
243nm
3.0nm
e-
e+
Notes: At first , we show you the property of e+e- pair production in the generator level.
At the beam crossing, produced incoherent e+e- paris are scattered to some way by the electrical field of another beam.
Since the beam is extremely focused in vertical direction, the opposite charged particles are scattered at larger angles especially vertical directions
Figure shows a scattered angle of electrons and positrons produced by the incoherent e+e- pair production for the electron beam.
You can see that positrons scattered larger angles in the vertical direction.
These electrons and positrons are boosted to a beam direction. It will depends on the angle of crab crossing.
We compared for several crossing angles.

## Slide 5: Property of e+e- pair production
e+e- pair production (CAIN incoherent pair data)
For all e+/e-
TRC500-20mrad
Inner R=15mm at B=3T
Detector Acceptance
|Cos| < 0.96
Pt vs |cos|
Pt
|cos|
Notes: This figure shows the 2D-plot of the transverse momentum versus cosine angle of produced e+e- pair for 20mrad crossing angle case.
Figure shows, if we assume that the detector coverage of cosine angle is less than 0.96, and the minimum transverse momentum of about 7MeV, we have still tail of the e+e- pair backgrounds.
Right figure shows the cos theta and Pt of e+e- pair for various crossing angles. The crossing angle gives a transverse momentum to the main beam, so that the Pt distribution of produced e+e- pair also has more Pt as larger crossing angle.
P=0.3Br:
B=3T/r=24mm/2 : P=10.8MeV
B=3T/r=15mm/2 : P=6.75MeV
B=4T/r=15mm/2 : P=9.0 MeV

## Slide 6: Property of e+e- pair production (cont.)
Pt dependence
with acceptance cut of |cos|<0.96
Crossing Angle dependence
with VTX acceptance cut
Not a significant dependency of crossing angle is observed.
But, Hit at VTX involve effect of (1)Geometrical effects (2)curling tracks (3)secondary particles produced in materials
R=15mm, B=3T [cos<0.96,Pt>6.75MeV]
R=15mm, B=4T [cos<0.96,Pt>9MeV]
R=24mm, B=3T [cos<0.90,Pt>10.8MeV]
tracks/Bunch
Notes: The vertex detector will be affected by the background condition in which the vertex detector is really installed.
So, I applied cosine angle cut to the CAIN data, and countered number of tracks.
Figure shows the Pt distribution after applying the cosine angle cut of less than 0.96 for different crossing angles.
If the both acceptance cut of Pt and cos theta were applied, the number of particles per a bunch becomes like right Figure.
We have not seen a significant dependency of crossing angle, however, actual hit on VTX detector involves effect of geometrical effects, curling tracks,
and secondary particles produced in materials.

## Slide 7: Hits on the VTX detector
JUPITER: the detector simulator
Study items
  B-Field dependence (3Tesla/4Tesla)
  Crossing angle dependence (0mrad/7mrad/20mrad)
CAIN+JUPITER
Interaction Region designs
  With L*=3.5m w Super-QC
  With L*=3.5m w Compact-QC
Notes: To take into account such effects, we have performed a full detector simulator connected to CAIN generator.
As study items, we tried detector field dependences, and crossing angle dependence.
For the design of interaction region, the L* is chosen to 3.5m with Super QCS.
But the design around QCS is different for small crossing and large crossing.

## Slide 8: IR and VTX designs
VTX detector
5Layer
1st Layer R=15mm
dZ= 50mm
CCD based
100um thick
30um active layer
CAL
SOL (3 or 4 Tesla) Uniform field was assumed.
Beam pipe
R =11mm dR=0.5mm
dZ=100mm
Beryllium
Beam pipe
R =73mm dR=2mm
Aluminum
WSiCAL
LowZ
For small crossing,0mrad/7mrad
incoming
beam
downstream
Inner/Outer radii 8cm/16.5cm QC
Inner/Outer radii 1cm/5.5cm QC
L*=3.5m
downstream
incoming
beam
For large crossing, 20mrad
Notes: This is a schematic view of the detector installed in JUPITER detector simulator.
Beam pipe is a radius of 11mm and 10cm half length beryllium connecting to 73mm radius Aluminum pipe.
These are WSiCal filled with Tungsten, and these are also tungsten masks.
In the design around QCS are changed according to the crossing angle due to space limitation.
For small angle, wide inner radius QCS is assumed, which inner and outer radii are 8 cm and 16,5 cm, respectively.
For large angle, compact QCS is assumed, which inner and outer radii are 1cm and 5.5cm, respectively.
In the small angle case, the extracted beam is also passing inside QCS, while in the larger angle case,
extracted line separated from QCS.
In the front of QCS, low Z material is attached as an XXXXX Mask.
The SOL give a uniform detector field in dZ < 340 cm,
VTX detector is consists of 5 layers which inner most radius of 15 cm, and radius of outer most layer is 63mm.
The thickness of sensor is 100um in which active layer is 30um. We counter the number of hits in the 30um active layer.

## Slide 9: Example Event display
20mrad crossing Disrupted beam
Notes: This is a example of event display for the disrupted beam events.

## Slide 10: Example Event Display
20mrad incoherent ee-pair
Notes: This is a example of event display for the incoherent ee pair events.

## Slide 11: Hit density at VTX
Crossing Angle | VTX Radius | Solenoid Field | Hit density
Head-on | 15mm | 4Tesla | 0.99
7mrad | 15mm | 4Tesla | 1.00
7mrad | 24mm | 3Tesla | 0.38
20mrad | 15mm | 4Tesla | 1.03
20mrad | 15mm | 3Tesla | 1.71
Hit densities are given in the unit of [/mm2/train]
Hit density on 1st Layer
Changing Solenoid field from 3 to 4 tesla
can suppress background effectively.
Estimated value of hit densities are
similar. No significant crossing angle
dependency has been observed.
Hit density at 1st layer is relatively high,
and at outer layer is not a problem.
Electrons energy at 1st Layer
In 1 year operation(107s),
1.5x1011/cm2/year at 1st Layer is estimated.
Hit densities at layers
20mrad/15mm/4Tesla
20mrad/15mm/4Tesla
(Number of hit, not pixels)
1
2
3
4
5
Notes: Hit Densities are calculated by counting the hit in active layer of 30micron thickness.(Not a pixel hits)
This table shows value of hit densities at the 1st layer for different crossing angles and detector field.
By changing detector field from 3 to 4 tesla, the hit density is suppressed effectively, and become about a half of value.
For the crossing angle, there is no significant dependency has been observed.
Right figure shows a track energy which hits the 1st layer, and hit densities for each layers.
Hit density of 1 st layer is very high and hit density at the other layers are not problem.
For the first layer, one year operation gives 1.5x10+11/cm2/year

## Slide 12: Hit position
Hit positions at 1st Layer (R=15mm)
X-Y view
Ladder
Z position
Hit density is smaller at the Z edge of detector, because the main source of electron come from IP. (small backscattering contamination)
0
1
2
3
4
5
6
7
Notes: These figure shows hit positions.
For the first layer, the ladder dependence and Z dependence.

## Slide 13: Origin of hit (20mrad)
Origin (%) | Head-on | 7mrad | 20mrad
IP | 9４ | 94 | 96
CCD | 2 | 2 | 2
Beam pipe | 2 | 1 | 2
Low Z,QC | 2 | 3 | <1
R=15mm,4Tesla
1st Layer hit origin (%)
QCS’s edge
Surface
of Low-Z mask
Beam pipe
Backscattering trapped by detector field
Secondary particles are produced at CCD itself, Beam pipe, and downstream of the beam line. Those contaminations are small about 5%.
Secondary particles have ~ a few MeV.
Trapped by detector field and back to the detector.
QCS’s edge is interference to the spread-out extracted beam.

## Slide 14: Upstream background Beam Delivery System
A full simulation program based on Geant4
has been developed to simulate the entire BDS.
Roadmap 2003
Tanabe/Aihara
Crossing 6mrad.
L* = 3.5m
The components ~ 200.
BDS-SIM
Background
(1) Synchrotron radiation photon
(2) Muon from lost halo electrons

## Slide 15: BDS-SIM: Synchrotron Radiation
Spatial distribution of SR photons arising from beam halo, at IP.
<E> = 4.76 MeV
Beam halo is assumed to have a uniform distribution.
Photons reaches to IP are produced mainly at FF quadrupole and last bending magnet.
These photons are predominantly contained within beam pipe, normaly ~ 1.cm.
~8mm
1cm

## Slide 16: BDS-SIM: Muon Background
Muons are produced predominantly at collimator section,
but the most of the muons are absorbed before reaching the IP.
Muon creation point.
Number of electrons required to hit the collimators /Muons at detector(16x16x16m3)
Iron pipes are effective to reduce muon backgrounds originating from collimators.

## Slide 17: Summary
e+e- pair background for the VTX detector has been studied.
  At 20mrad crossing angle, hit density is estimated to be about 1.0/mm2/train. This is corresponding to 1.5x1011/cm2/year.
  Main background source of e+e- pair comes from interaction points directly.
  There is no significant differences for the VTX, even crossing angle is widen up to 20mrad.
  The e+e- pairs hit QC at downstream, so that the consideration of arrangement will be necessary, as well as the design of beam dump line.
Upstream background
  Synchrotron radiation and Muon backgrounds has been studied using Geant4 based Beam delivery simulator.
  Further study with updated BSD design and with detector simulator is desirable. This work will gives an answer about a precise estimation of neutron background from extraction line.

## Slide 18: Introduction
Background for Vertex detector
  Synchrotron radiation
    Secondary particles, electrons and neutrons
  Beam-Beam interaction
    e+e- pair production
  Two-Photon interaction
    Charged hadrons
Influence of background on CCD based VTX
  Radiation damage
    Non Ionizing Energy Loss increases CTI
      Caused by high energy charged particles
      Depends on the particle energy
Notes: For the vertex detector, three types of backgrounds should be taken into account.
Those are, Synchrotron radiation, beam-beam interaction as accelerator incidental,
and the low-mass two-photon interaction events as a physics incidental events.
These processes produce charged particles, directly or indirectly.
Most serious influence of the background to the CCD based VTX detector is
the increase of charge transfer inefficiency due to Non-Ionizing Energy loss process.
It is caused by the charged particles, and depends on the energy of particles.

## Slide 19: Pair distribution at Z=330cm, B=4T
Energy flow in 0.5mm square mesh / bunch
0mrad electron
0mrad positron
7mrad positron
7mrad electron
20mrad electron
20mrad Positron
GeV
100TeV
100GeV
1GeV

## Slide 20: Pair distribution at Z=330cm,B=0T
0mrad Electron
0mrad Positron

## Slide 21: Track Energy density
7mrad crossing / 4Tesla
20mrad crossing / 4Tesla
GeV/mm2/train
Electrons
Positrons
Electrons
Positrons
Z (cm)
Radius (cm)

## Slide 22: Hit origin
0mrad,B4,R15
Beam pipe
L*=3.5m

## Slide 23: BDS-SIM: Synchrotron Radiation
Spatial distribution of SR photons arising from nominal beam at IP
width ~ 0.5mm
<E> = 0.35MeV
Wider and long tail distribution in x-direction is due to photons generated at the bending magnets.
Photons reaches to IP are mainly produces at FF quadrupole and the last bending magnet.
Photons are predominantly contained within beam pipe.