*
* $Id: mat.doc,v 1.1.1.1 1995/10/24 10:19:51 cernlib Exp $
*
* $Log: mat.doc,v $
* Revision 1.1.1.1  1995/10/24 10:19:51  cernlib
* Geant
*
*
*CMZ :  3.21/02 29/03/94  15.41.37  by  S.Giani
*-- Author :
C**
C** ALL MATERIAL CONSTANTS ARE PARTLY STORED ON THE COMMON /MAT IN THE
C** BLOCK DATA OR CALCULATED IN THE ROUTINE MATTER.IN PRESENT VERSION
C** THERE MAY BE DEFINED UP TO 20 MATERIALS WITH THE MATERIAL-INDEX
C** NUMBER 'IND' . THIS MATERIAL INDEX NUMBER MUST BE GIVEN FOR
C** EACH CELL OF A CALORIMETER IN THE GEOMETRY INPUT DATA CARDS.
C** (SEE COMMON /CALSTR AND INIT). IND =0 IS ALWAYS INTERPRETED AS
C** VACUUM IN THE PROGRAM.
C
C** DEN   (IND+1) =  DENSITY (GR/CM**3)
C** RADLTH(IND+1) =  RADIATION LENGTH (CM)
C** ATNO  (IND+1) =  ATOMIC NUMBER (AVERAGE VALUE, SEE LATER)
C** ZNO   (IND+1) =  CHARGE NUMBER OF NUCLEUS (AVERAGE VALUE, SEE LATER)
C** ABSL  (IND+1) =  ABSORPTION LENGTH (ONLY USED FOR STEP SIZE
C**                  CALCULATION)
C** CDEN  (IND+1) =  C - PARAMETER IN STERNHEIMERS THEORY
C** MDEN  (IND+1) =  M - PARAMETER IN STERNHEIMERS THEORY
C** X0DEN (IND+1) =  X0- PARAMETER IN STERNHEIMERS THEORY
C** X1DEN (IND+1) =  X1- PARAMETER IN STERNHEIMERS THEORY
C** RION  (IND+1) =  IONISATION POTENTIAL
C** MATID (IND+1)    =  GHEISHA ALPHANUMERIC LABEL (A4)
C** MATID1(IND+1,24) =  EGS ALPHANUMERIC LABEL (24*A1)
C**   10 PARAMETERS DESCRIBING THE MATERIAL AT VARIOUS PLACES
C**   IN THE PROGRAM :
C** PARMAT(IND+1, 1) = X    DE/DX CORRECTION FACTOR FOR LANDAU
C**                         TYPE DISTRIBUTIONS
C** PARMAT(IND+1, 2) = 1.   FOR SOLIDS
C**                  = 2.   FOR FLUIDS
C**                  = 3.   FOE GASEOUS MATERIALS
C** PARMAT(IND+1, 3) = 1.   DELTA-RAY SELECTION : ALL PARTICLES
C**                  = 2.   DELTA-RAY SELECTION : ONLY MUONS
C**                  = 3.   DELTA-RAY SELECTION : MUONS AND ELECTRONS
C**                  = 4.   DELTA-RAY SELECTION : MUONS,ELECTRONS,PIONS
C** PARMAT(IND+1, 4) =      MINIMUM RANGE FOR DELTA-ELECTRONS
C** PARMAT(IND+1, 5) = 1.   FOR ANORGANIC SCINTILLATORS ONLY
C** PARMAT(IND+1, 6) =      SATURATION COEFFICIENT IN BIRK'S LAW
C**                  = 1.   DEFAULT VALUE  SAT=0.010/DENSITY,
C**                  > 1.                  SAT=PARMAT(IND+1,6)-1.
C** PARMAT(IND+1, 7) > 0.   INDUCED HADRON NUCLEAR FISSION
C** PARMAT(IND+1, 8) > 0.  PHOTOABSORBTION AND PHOTOFISSION
C** PARMAT(IND+1, 9) > 0.  NATURAL RADIOACTIVITY
C** PARMAT(IND+1,10) =     CORRECTION FACTOR FOR ENERGY LOSS BY
C**                        NUCLEAR BREAKUP EFFECTS
C**                  = 0.  DEFAULT MODEL DESCRIPTION IS USED.
C**
C**    THE DENSITY, ATOMIC NUMBER AND CHARGE NUMBER , DEFINED ABOVE,
C**    ARE AVERAGE VALUES FOR COMPOUND MATERIALS LIKE BGO.
C**    THESE VALUES ARE USED FOR DE/DX- CALCULATIONS ONLY.
C**
C** ALL MATERIALS MAY BE DEFINED AS COMPOUNDS OR MIXTURES,
C** THE FOLLOWING NUMBERS ARE TAKEN FROM THE EGS DATA FILE,
C** OR, IF NOT GIVEN, CALCULATED.
C** IFRAC(J)      = NUMBER OF COMPOUNDS IN THIS MATERIAL
C** FRAC1(J,I)    = PARTIAL INTERACT.LENGTH OF THE I.TH COMPOUND
C** DEN1 (J,I)    = PARTIAL DENSITY   OF THE I.TH COMPOUND
C** ATNO1(J,I)    = ATOMIC NUMBER     OF THE I.TH COMPOUND
C** ZNO1 (J,I)    = CHARGE NUMBER     OF THE I.TH COMPOUND
C**
C**