*
* $Id: result.doc,v 1.1.1.1 1995/10/24 10:19:51 cernlib Exp $
*
* $Log: result.doc,v $
* Revision 1.1.1.1  1995/10/24 10:19:51  cernlib
* Geant
*
*
*CMZ :  3.21/02 29/03/94  15.41.37  by  S.Giani
*-- Author :
C**
C** THE RESULT COMMON STORES ALL INFORMATION OF THE CURRENT TRACK:
C**
C** XEND    |    START- OR END- COORDINATES OF THE CURRENT STEP.
C** YEND    |
C** ZEND    |
C** RCA          CALO1*1000.+CALO2*1.  |CALO1 AND CALO2 (CELL1 AND
C** RCE          CELL1*1000.+CELL2*1.  |CELL2) ARE THE CALORIMETER
C**                                    |(CELLS), WHERE THIS STEP COMES
C**                                    |FROM AND GOES TO.
C** AMAS         MASS
C** NCH          CHARGE
C** TOF          TIME OF FLIGHT  (IN 1/20 NSEC)
C** PX           PX/P = COSL*COSP
C** PY           PY/P = COSL*SINP
C** PZ           PZ/P = SINL
C** USERW        USERWORD (SEE 'HSTORY')
C** INTCT        INTERACTION/DECAY-COUNTER
C** P            MOMENTUM
C** EN           TOTAL ENERGY
C** EK           KINETIC ENERGY
C** AMASQ        MASS**2
C** DELTN        ACTUAL STEPSIZE  (SEE ALSO DDELTN IN COMMON /CURPAR)
C** ITK          NUMBER OF GENERATOR TRACK (SEE INPUT-ROUTINES)
C** NTK          NUMBER OF TRACK IN SHOWER
C** IPART        PARTICLE INDEX (SEE #MASIND)
C** IND          MATERIAL INDEX (SEE #MATTER)
C** LCALO        CALORIMETER NUMBER (=CALORIMETER1 IN RCA)
C** ICEL         CELL NUMBER        (=CELL1 IN RCE)
C** SINL         SINE OF DIP-ANGLE
C** COSL         COSINE OF DIP-ANGLE
C** SINP         SINE OF NORMAL PHI-ANGLE (WITH RESPECT TO X-AXIS)
C** COSP         COSINE OF NORMAL PHI-ANGLE
C**